## Slide 1: Dissertation Title: 3D Object Shape Recognition and Motion tracking for Robotic pick and place application Sai Mohanty – 2022AA05245

## Slide 2: Addressing Review comments
Review Comments Given | Work done
Check the need for LLM in to the model . Project objective contradicts with the proposed design overview | Removed LLM from the overall application as it does not serve any purpose w.r.t the project topic.
Plan for Python friendly robo simuation tool for model implementation & testing | Gazebo robot simulator will be used. This has Python APIs to publish and subscribe data . https://classic.gazebosim.org/tutorials?tut=drcsim_ros_python&cat=drcsim
Finalize on the data set & features . Instead of pre-structured dataset , create a front end that can feed images by upload | Finalize on data set (slide 7) and added a gui front end to feed image in the application flow.
Focus on 3-4 research paper no older than 6 months and relook on best way to do literature review | Did not find research paper < 6 months old but referred 2023, 2022 research papers.
MLOps proposed as second objective in the project is not clearly defined as process in the document or in presentation . | Prepared MLOps flow for the project (slide 5)
Implement DRL based models to let the model learn the shapes | Did went through research papers and videos to understand DRL for object detection. Changed the same in abstract file. (refer slide 4)

## Slide 3: Design Solutions in Next Slides

## Slide 4: Model Block Diagram
GUI Interface
Image dataset upload
Video file upload
Image Pre-Processing
Object Segmentation using Deep Reinforcement Learning
Motion Estimation using Optical Flow
Code for publishing object coordinates and shape information
Visualization of segmented object and motion coordinates

## Slide 5: MLOps Flow
Model Training
Frame input
Model Validation & Evaluation
Model Packaging
Model Registry
Deployed Model
Model Monitoring
Alert Manager
Docker Container

## Slide 6: MLOps Flow
Model Inference
Model Registry using MLFLOW API
Docker Container
Model Code
Minio db
influx db
Web App
Meta data Publisher to ROS2
Datastore

## Slide 7: Application Block Diagram
Model Block Output
- Object shape and motion coordinates
Python Publisher script for publishing coordinates using Gazebo API
Gazebo API
Gazebo Robot Simulator
MLOps Block
Open-Source Component

## Slide 8: Data Set
COCO 2017 dataset to be used.
- As unsupervised learning will be used, so test dataset(40k image files) and validation dataset(5000 image files) will be used that are unlabeled.
- Link to dataset: https://www.kaggle.com/datasets/awsaf49/coco-2017-dataset/data

## Slide 9: Setup
ROS2
Node 1
Node 2
System connected with camera and running Algo
System simulating Robot Arm using Gazebo simulator

## Slide 10: Architecture Diagram
Web App
Image File Upload
Video file upload
Camera Stream Input
Static Object Detection Model
Motion Detection and Motion Tracking Model
ROS2 Publisher Script
Model Registry
ROS2 Subscriber Script
ROS2 Communication
Node 1
Node 2
Container 1
Container 2
Data Store
influxdb
minio
Image and meta data store
Model version management

## Slide 11: Static Object Detection Model Pipeline
Image File Input
Conversion to GrayScale
Smoothing - Gaussian Blur
Canny Edge Detection
Finding Contours
Calculate bounding box, Center coordinates, orientation using PCA
Draw BB, apply text and resize to focus on detected object
Send the data and image to ROS2 Publisher topic /staticobjectdata and /staticobject
Save detected image and meta data to datastore

## Slide 12: Motion Detection and Tracking Model Pipeline
Video File Input
Apply Background Subtractor
Get Foreground mask
Detect moving object using background subtractor technique
Finding Contours
Calculate bounding box, Center coordinates, current position
Calculate Speed of the object in each frame and average speed of moving object
Send the data and image to ROS2 Publisher topic /staticobjectdata and /staticobject
Draw BB, put text on the detected object image
Save detected image and meta data to datastore

## Slide 13: Anomaly Detection Model Pipeline
Offline Capture frames with normal data and store in local folder
Image preprocessing
OneClass SVM Model Training
One Class SVM Predict
Report Anomalous
Continuous Frame Input

## Slide 14: Containerization
Containerized Model
WebApp
MQTT Broker
Docker Container 1
Docker Container 2
Docker Container 3

## Slide 15: Web Application
Image File Upload
Video File Upload
RTSP Stream Input URL
Display Input image/video
Display Detected Object/Motion tracked image/video
Display meta data
Run Detection/Motion Tracking Model
Button
Button
User Input
Button
Display Output Field
Display Output Field
Display Output Field
Static object detection model
Motion Detection/Tracking Model
Backend logic to choose the model

## Slide 16: Current Setup
Side view of camera
Moving Conveyor belt
Object to be picked
Edge Device
Robotics Arm
Object Detection/Motion Track Model
Camera

## Slide 17: New Setup
Top view of camera
Moving Conveyor belt
Object to be picked
Edge Device
Robotics Arm
Object Detection/Motion Track Model
Camera